## Slide 2
Canara Lighting is a pioneer in TV Studio lighting solutions with many prestigious projects executed over the past 50 years. Our extensive knowledge and expertise gained over the years makes us the ideal partner to work on projects from concept to commissioning with extensive training and after sales service. Our solutions are engineered to meet each customer's individual requirements. No matter the size of the studio or its unique requirement, Canara is your partner for the perfect lighting solution.
Canara Lighting has been serving the exacting and changing needs of our customers for the last 50 years. We have a world class manufacturing facility at Mangalore which is the largest in South Asia and includes R&D and testing facilities for lights and rigging. We truly follow the 'Make in India' concept in word and spirit. We provide turnkey lighting solutions for broadcasting studios, film studios, auditoriums, stadiums, sound and light shows, façade lighting and musical fountains. We provide world class products supported by effective service all over the country. All leading TV channels, auditoriums, convention centers are equipped with the knowledge and lighting solutions from Canara Lighting.
Contact us at :
info@canaralighting.com / contact@canaralighting.com
+91 95912 77022/ +91 95913 55022
www.canaralighting.com

## Slide 3
INDEX-1
TABLE OF CONTENTS |  |  | 
SL NO | PRODUCT DESCRIPTION | PAGE NO | REMARKS
STUDIO GRID & RIGGING SYSTEM |  |  | 
1 | FIXED PIPE GRID |  | 
2 | TRACK BEAM SYSTEM |  | 
3 | MOTORISED FLYGRIDS |  | 
4 | MOTORISED TELECLIMBERS |  | 
5 | MANUAL PANTOGRAPHS |  | 
6 | MOTORISED PANTOGRAPGHS |  | 
7 | EXTENDERS |  | 
STUDIO CURTAINS, CHROMA & CYCLORAMA |  |  | 
8 | PERIPHERAL CURTAIN TRACKS |  | 
9 | CHROMA SCREENS |  | 
10 | CYCLORAMA SCREENS |  | 
LIGHTING FIXTURES |  |  | 
11 | 90W, 5600K SOFT PANEL LIGHT |  | 
12 | 90W, 3200K SOFT PANEL LIGHT |  | 
13 | 90W, CCT TUNABLE SOFT PANEL LIGHT |  | 
14 | 150W, 5600K SOFT PANEL LIGHT |  | 
15 | 150W, 3200K SOFT PANEL LIGHT |  | 
16 | 150W, CCT TUNABLE SOFT PANEL LIGHT |  | 
17 | 180W, 5600K SOFT PANEL LIGHT |  | 
18 | 180W, 3200K SOFT PANEL LIGHT |  | 

## Slide 4
INDEX-2
TABLE OF CONTENTS |  |  | 
SL NO | PRODUCT DESCRIPTION | PAGE NO | REMARKS
19 | 180W, CCT TUNABLE SOFT PANEL LIGHT |  | 
20 | 250W, 5600K SOFT PANEL LIGHT |  | 
21 | 250W, 3200K SOFT PANEL LIGHT |  | 
22 | 250W, CCT TUNABLE SOFT PANEL LIGHT |  | 
23 | 90W, 5600K LENS PANEL LIGHT |  | 
24 | 90W, 3200K LENS PANEL LIGHT |  | 
25 | 90W, CCT TUNABLE LENS PANEL LIGHT |  | 
26 | 150W, 5600K LENS PANEL LIGHT |  | 
27 | 150W, 3200K LENS PANEL LIGHT |  | 
28 | 150W, CCT TUNABLE LENS PANEL LIGHT |  | 
29 | 180W, 5600K LENS PANEL LIGHT |  | 
30 | 180W, 3200K LENS PANEL LIGHT |  | 
31 | 180W, CCT TUNABLE LENS PANEL LIGHT |  | 
32 | 250W, 5600K LENS PANEL LIGHT |  | 
33 | 250W, 3200K LENS PANEL LIGHT |  | 
34 | 250W, CCT TUNABLE LENS PANEL LIGHT |  | 
35 | 100W, 5600K FRESNEL SPOT LIGHT |  | 
36 | 100W, 3200K FRESNEL SPOT LIGHT |  | 
37 | 200W, 5600K FRESNEL SPOT LIGHT |  | 
38 | 200W, 3200K FRESNEL SPOT LIGHT |  | 
39 | 200W, CCT TUNABLE FRESNEL SPOT LIGHT |  | 

## Slide 5
INDEX-3
TABLE OF CONTENTS |  |  | 
SL NO | PRODUCT DESCRIPTION | PAGE NO | REMARKS
40 | 200W, COLOR TUNABLE FRESNEL SPOT LIGHT |  | 
41 | 400W, 5600K FRESNEL SPOT LIGHT |  | 
42 | 400W, 3200K FRESNEL SPOT LIGHT |  | 
43 | 200W LED JAGLE PANEL LIGHT |  | 
44 | 400W LED JAGLE PANEL LIGHT |  | 
45 | 60W 5600K LED ENG LIGHT |  | 
46 | 60W 3200K LED ENG LIGHT |  | 
47 | 60W CCT TUNABLE LED ENG LIGHT |  | 
48 | 150W CYCLORAMA WASH LIGHT |  | 
49 | 200W, 3200K FIXED BEAM PROFILE SPOT LIGHT |  | 
50 | 200W, RGBW FIXED BEAM PROFILE SPOT LIGHT |  | 
51 | 200W, 3200K ZOOM PROFILE SPOT LIGHT |  | 
52 | 200W, RGBW ZOOM PROFILE SPOT LIGHT |  | 
53 | 300W, 3200K FIXED BEAM PROFILE SPOT LIGHT |  | 
54 | 300W, RGBW FIXED BEAM PROFILE SPOT LIGHT |  | 
52 | 300W, 3200K ZOOM PROFILE SPOT LIGHT |  | 
53 | 300W, RGBW ZOOM PROFILE SPOT LIGHT |  | 
54 | 54 X 3W RGBW PAR LIGHT |  | 
55 | 54 X 3W 5600K PAR LIGHT |  | 
56 | 54 X 3W 3200K PAR LIGHT |  | 
57 | 54 X 3W BI COLOR PAR LIGHT |  | 

## Slide 6
INDEX-4
TABLE OF CONTENTS |  |  | 
SL NO | PRODUCT DESCRIPTION | PAGE NO | REMARKS
58 | 18 X 10W RGBW PAR LIGHT |  | 
59 | 150W CHROMA WASH LIGHT |  | 
60 | 20W 3200K MINI PROFILE LIGHT |  | 
SPLITTERS & CONSOLE |  |  | 
54 | 8 CHANNEL RDM DMX AMPLIFIER SPLITTER |  | 
55 | 96 FIXTURE NON RDM LIGHTING CONSOLE |  | 
56 | 96 FIXTURE RDM LIGHTING CONSOLE |  | 
57 | 120 FIXRURE RDM LIGHTING CONSOLE |  | 
58 | 200 FIXTURE RDM LIGHTING CONSOLE |  | 
59 | 512 FIXTURE NON RDM LIGHTING CONSOLE |  | 
60 | 96 FIXTURE NON RDM LIGHTING CONSOLE |  | 
61 | 48 FIXTURE TOUCH SCREEN LIGHTING CONSOLE |  | 
62 | 96 FIXTURE TOUCH SCREEN LIGHTING CONSOLE |  | 
63 | 2048 FIXTURE TOUCH SCREEN LIGHTING CONSOLE |  | 
MISCELLANIOUS ITEMS |  |  | 
64 | POWER JUNCTION BOXES |  | 
65 | SIGNAL JUNCTION BOXES |  | 
66 | CABLE TRAYS |  | 
67 | POWER DISTRIBUTION PANELS |  | 
52 | MOTOR CONTROL PANELS |  | 
53 | MS PIPE, C TRACK & SUSPENDERS |  | 

## Slide 7
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
FIXED PIPE GRID
Canara fixed pipe grid offers a wide range of design options to suspend the lighting fixtures in Theaters, Auditoriums and Convention centers, Studios, Production House, Film Institutions.
SPECIAL FEATURES
Designed with the highest standards of construction using 40NB MS tubes duly epoxy polyester powder coated in black matt texture finish.
Pipe grid is constructed in different sizes: 1X1, 1.2X1.2, 1.5X1.5, 2X2 Mrt. The grid is suspended using M12 threaded rod suspenders or angle suspenders.
Pipe grid is permanently mounted approx. 2 ft. below ceiling and lighting fixtures can be hung, adjusted and maintained from floor using clamps, flexi-adaptors and pole operated yoke systems of light fixtures.
TECHNICAL SPECIFICATIONS
Standard Dimensions : 1X1 Meter, 1.2X1.2 Meter, 1.5X1.5 Meter, 2X2 Meter, Customizable,
Safe Working Load : 80 kg
Pipe Specification : 40 Nominal Bore, 2mm / 3mm thick, 48mm Outer diameter
7 Tank chemical treatment to keep away from rust
1 of 1
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
PRODUCT CODES : FPG-1, FPG-1.2, FPG-1.5, FPG-2

## Slide 8
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TRACK BEAM GRID
Canara fixed pipe grid offers a wide range of design options to suspend the lighting fixtures in Theaters, Auditoriums and Convention centers, Studios, Production House, Film Institutions.
SPECIAL FEATURES
Designed with the highest standards of construction using Aluminium I-tracks duly epoxy polyester powder coated in black matt texture finish.
Track grid is constructed in different sizes: 1X1, 1.2X1.2, 1.5X1.5, 2X2 Mrt. The grid is suspended using M12 threaded rod suspenders or angle suspenders.
Pipe grid is permanently mounted approx. 2 ft. below ceiling and lighting fixtures can be hung, adjusted and maintained from floor using clamps, flexi-adaptors and pole operated yoke systems of light fixtures.
TECHNICAL SPECIFICATIONS
Standard Dimensions : 1X1 Meter, 1.2X1.2 Meter, 1.5X1.5 Meter, 2X2 Meter, Customizable,
Safe Working Load : 80 kg
Swivel trolley for flexible movement of Tracks & Medium duty track trolleys for Light positioning
7 Tank chemical treatment to keep away from rust
1 of 1
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
PRODUCT CODES : TBG

## Slide 9
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
Motorized Flygrid combines innovative design with the highest standards of construction and ease of installation for payloads up to 180Kg. Motorized Flygrid incorporates the luminaire suspension pipe, the relevant safety switches luminaire power outlet, and a worm geared motor raising and lowering the unit. To reduce the costs of the site installation and simplify it, the Hoist is supplied with pre-mounted structure to which the four wire ropes, the flip-flop power cable tray and electrical terminal box are already attached.
SPECIAL FEATURES
EFFICIENCY AND OPERATING COSTS : The Self Climbing hoist is ideal for the raising and lowering of lighting instruments along with their associated circuits and dimmers. The ability to lower the lighting batten to any positions within the set area, increases the efficiency of the operations by allowing easy access to the lighting instruments for aiming, focusing and the handling of the lighting fixtures, This product can be either installed in permanent fixed positions directly to the I-beam sub-structure of the building, or to any supporting grid
Certifications : CE
MECHANICAL : A special frame maintains a clear separation between the moving parts (mechanical elements in motion), like steel ropes, winding discs, diverter pulleys, load sensor mechanisms) and the electrical components (electrical wiring, motor switch-gears, safety micro switches, electrical and data sockets, travel limit device). The separation of these elements allows maintenance procedures to be performed safely and the electrical components maintained in a clean environment.
1 of 2
MOTORIZED FLYGRID

## Slide 10
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
2 of 2
TECHNICAL SPECIFICATIONS
Electric Motor : 0.75 HP/ 1.0 HP / 1.5 HP, 3 Phase AC Motor with DC Brake
Gear Box : Specially designed single stage worm reduction
Self Weight : >250 kg
Safe Working Load : 180kg to 200kg
Max Travel Distance : upto 13 Meter (Standard) or More as per the requirement
Lift speed : 5 to 7 Meter / Minute
Minimum Collapse Height : 1.4 Meter
Safety : Two safety micro switches each for the Top and the Bottom limit, Slack wire safety, Over load protection
Lifting rope : 4 Nos 4mm diameter anti-rotating GI ropes
Finish : Epoxy polyester powder coated in matt texture finish
Control : DOL with forward and reverse control (Standard approach )
Optional Control : VFD / Wireless / HMI / Hand-held Pendent
Grid Size : 2X2, 2.5x2.5, 3X3, 4X4 Meter (Customizable as per site requirements)
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
PRODUCT CODES : MFG 22, MFG 252, MFG 2525, MFG 253, MFG 32, MFG 33
STANDARD SAFETY FEATURES
SAFETY : Approved by the testing authorities of the European standards. These Standards are directly associated with safety of suspensions systems mounted above an assembly of people. The safety features incorporated into the Canara motorised Flygrid, a dynamic self sustaining worm-geared set motor with DC brake and screw helix angle less than 4 degrees to prevent back winding, two safety micro switches one for the top limit plus an extra emergency safety switch and one for the bottom limit plus an extra emergency safety switch and over load and slack line detection on each wire rope.
OPERATIONAL : The Self-Climbing Hoist is capable of lifting a safe working load (SWL) of 180 Kg, plus the self-weight of the hoist, which is based on the travel distance and the optional features incorporated into the hoist. The maximum travel distance is 42 feet /13 meters (Standard) or More as per the requirement.
MOTORIZED FLYGRID

## Slide 11
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
Motorized Teleclimber combines innovative design with the highest standards of construction and ease of installation for payloads up to 140Kg. Motorized Teleclimber incorporates the luminaire suspension pipe, the relevant safety switches luminaire power outlet, and a worm geared motor raising and lowering the unit. To reduce the costs of the site installation and simplify it, the Hoist is supplied with pre-mounted structure to which the four wire ropes, the flip-flop power cable tray and electrical terminal box are already attached.
SPECIAL FEATURES
EFFICIENCY AND OPERATING COSTS : The Self Climbing hoist is ideal for the raising and lowering of lighting instruments along with their associated circuits and dimmers. The ability to lower the lighting batten to any positions within the set area, increases the efficiency of the operations by allowing easy access to the lighting instruments for aiming, focusing and the handling of the lighting fixtures, This product can be either installed in permanent fixed positions directly to the I-beam sub-structure of the building, or to any supporting grid
Certifications : CE
MECHANICAL : A special frame maintains a clear separation between the moving parts (mechanical elements in motion), like steel ropes, winding discs, diverter pulleys, load sensor mechanisms) and the electrical components (electrical wiring, motor switch-gears, safety micro switches, electrical and data sockets, travel limit device). The separation of these elements allows maintenance procedures to be performed safely and the electrical components maintained in a clean environment.
1 of 2
MOTORIZED TELECLIMBER

## Slide 12
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
2 of 2
TECHNICAL SPECIFICATIONS
Electric Motor : 0.75 HP/ 1.0 HP / 1.5 HP, 3 Phase AC Motor with DC Brake
Gear Box : Specially designed single stage worm reduction
Self Weight : > 145 kg
Safe Working Load : 100kg to 145kg
Max Travel Distance : upto 13 Meter
Lift speed : 5 to 7 Meter / Minute
Minimum Collapse Height : 1.4 Meter
Safety : Two safety micro switches each for the Top and the Bottom limit, Slack wire safety, Over load protection
Lifting rope : 4 Nos 4mm diameter anti-rotating GI ropes
Finish : Epoxy polyester powder coated in matt texture finish
Control : DOL with forward and reverse control (Standard approach )
Optional Control : VFD / Wireless / HMI / Hand-held Pendent
Winch Length : 2.5 Meter to 5 Meter (Customizable as per site requirements)
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
PRODUCT CODES : TCH-CEE, TCH-IEC, TCH-CPL, TCH-BCH, TCH-CYC CEE, TCH-CYC CPL, TCH-CYC BCH, TCH-CYC IEC, TCH-CD, TCH-ID, TCH-BD, TCH-CPD, TCH-CID, TCH-BID, TCH-CPID, TCH-CB, TCH-IB, TCH-BB, TCH-CPB, TCH-CIB, TCH-BIB, TCH-CPIB
STANDARD SAFETY FEATURES
SAFETY : Approved by the testing authorities of the European standards. These Standards are directly associated with safety of suspensions systems mounted above an assembly of people. The safety features incorporated into the Canara motorised teleclimber, a dynamic self sustaining worm-geared set motor with DC brake and screw helix angle less than 4 degrees to prevent back winding, two safety micro switches one for the top limit plus an extra emergency safety switch and one for the bottom limit plus an extra emergency safety switch and over load and slack line detection on each wire rope.
OPERATIONAL : The Self-Climbing Hoist is capable of lifting a safe working load (SWL) of 140 Kg, plus the self-weight of the hoist, which is based on the travel distance and the optional features incorporated into the hoist. The maximum travel distance is 42 feet /13 meters.
MOTORIZED TELECLIMBER

## Slide 13
Canara LED Panel series LED lighting system has been specifically developed for film and video applications that demand extremely color-accurate, high quality light. Utilizing proprietary, state-of-the-art, daylight balanced LEDs, Canara LED Panel creates a high volume of broad spectrum white light, combined with an electronic flicker-free dimmable power supply unit to create a powerful yet economical LED soft light. Perfect for TV studio, Production Studios, Film Recordings & Documentaries etc.,
SOFT PANEL LIGHT
SPECIAL FEATURES
Delivers the High-volume light output.
Double accessories slot for inserting color Filters, Barndoor and other accessories with lock retaining clip.
Fully RDM Compliant when in DMX mode
Electronic universal power supply 100-260 V AC, 50/60 Hz.
Non-glare, diffuser provides uniform, single source light.
Efficient power and thermal management delivers low power consumption and enhanced reliability.
Fanless design perfect for studio application
All metal construction.
No light spill to distract audiences or performers.
Available with pole operated yoke.
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TECHNICAL SPECIFICATIONS
LIGHT SOURCE
Lamp : SMD LED ARRAY
Color temperature (CCT) : 5600K
CRI : > 95, TLCI: > 95, R9 Value: > 95
Color Quality Scale (CQS) : > 95
Lamp life : L70 >50000 Hours @ 55°C
OPTICAL SYSTEM
Beam Angle : 100°
Acrylic milky diffuser 2 mm /3mm thick provides eye pleasant light output.
1 of 3
90W – 5600K
MODEL : CAN LED T

## Slide 14
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
ELECTRICAL
Flicker free auto-ranging electronic switch mode power supply 100~240 VAC Nominal, 50/60 Hz
0 to 100% 8 Bit Linear Dimming
Power Factor ≥0.95 @ 230V 50Hz
Main fuse - T12A-250V
Max mains current 3.7A@drawn 1A @ 230V 50Hz
Max LED current drawn 54V DC
Power supply cable: 2 meter 3 Core 1Sq mm FRLS grade PVC cable with IEC Plug
CONTROL
On board Control with 5 No's High Precision Membrane switch with 7 segment display for easy to read status.
USITT DMX512A (RDM Compatible) Control Protocol.
5 pin locking XLR Chasis mount DMX in & through connections
8 bit DMX control, extra soft dimming, for theatrical & Studio use.
PHYSICAL
Aluminum laser cut body
Passive Cooling system with large heatsink, no noise, perfect for TV studios & theatres
Aluminium yoke
Available in Manual and Pole operated system for Pan, Tilt and Focus.
Epoxy polyester powder coated matt black finish (RAL – 9005) (Customizable as per requirements)
IP Rating : IP20
DMX CHART
1 Channel Mode : Dimmer, 0-100%
WEIGHT & DIMENTIONS
 | Normal Yoke | POS Yoke | Unit
Weight | 7.6 | 9.8 | Kg
Length | 370 |  | mm
Width | 250 |  | mm
Height | 295 |  | mm
ACCESSORIES | 
 | 8 leaf Barndoor
 | 4 leaf Barndoor
 | Softbox
 | Honey comb screens
 | Filter frame
 | Clamps & Spuds
 | Cables
2 of 3
90W – 5600K

## Slide 15
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 5600K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 1.5 | 2 | 2.5 | 3
 | (ft) | 3.28 | 4.92 | 6.56 | 8.20 | 9.84
Beam Diameter | (m) | 2.39 | 3.58 | 4.77 | 5.96 | 7.16
 | (ft) | 7.84 | 11.75 | 15.65 | 19.55 | 23.49
Illumination | (lux) | 2000 | 889 | 500 | 320 | 222
 | (fc) | 186 | 83 | 46 | 30 | 21
POLAR DIAGRAM – FLOOD
PHOTOMETRIC PERFORMANCE
3 of 3
90W – 5600K

## Slide 16
Canara LED Panel series LED lighting system has been specifically developed for film and video applications that demand extremely color-accurate, high quality light. Utilizing proprietary, state-of-the-art, daylight balanced LEDs, Canara LED Panel creates a high volume of broad spectrum white light, combined with an electronic flicker-free dimmable power supply unit to create a powerful yet economical LED soft light. Perfect for TV studio, Production Studios, Film Recordings & Documentaries etc.,
SOFT PANEL LIGHT
SPECIAL FEATURES
Delivers the High-volume light output.
Double accessories slot for inserting color Filters, Barndoor and other accessories with lock retaining clip.
Fully RDM Compliant when in DMX mode
Electronic universal power supply 100-260 V AC, 50/60 Hz.
Non-glare, diffuser provides uniform, single source light.
Efficient power and thermal management delivers low power consumption and enhanced reliability.
Fanless design perfect for studio application
All metal construction.
No light spill to distract audiences or performers.
Available with pole operated yoke.
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TECHNICAL SPECIFICATIONS
LIGHT SOURCE
Lamp : SMD LED ARRAY
Color temperature (CCT) : 5600K
CRI : > 95, TLCI: > 95, R9 Value: > 95
Color Quality Scale (CQS) : > 95
Lamp life : L70 >50000 Hours @ 55°C
OPTICAL SYSTEM
Beam Angle : 100°
Acrylic milky diffuser 2 mm /3mm thick provides eye pleasant light output.
1 of 3
90W – 3200K
MODEL : CAN LED T

## Slide 17
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
ELECTRICAL
Flicker free auto-ranging electronic switch mode power supply 100~240 VAC Nominal, 50/60 Hz
0 to 100% 8 Bit Linear Dimming
Power Factor ≥0.95 @ 230V 50Hz
Main fuse - T12A-250V
Max mains current 3.7A@drawn 1A @ 230V 50Hz
Max LED current drawn 54V DC
Power supply cable: 2 meter 3 Core 1Sq mm FRLS grade PVC cable with IEC Plug
CONTROL
On board Control with 5 No's High Precision Membrane switch with 7 segment display for easy to read status.
USITT DMX512A (RDM Compatible) Control Protocol.
5 pin locking XLR Chasis mount DMX in & through connections
8 bit DMX control, extra soft dimming, for theatrical & Studio use.
PHYSICAL
Aluminum laser cut body
Passive Cooling system with large heatsink, no noise, perfect for TV studios & theatres
Aluminium yoke
Available in Manual and Pole operated system for Pan, Tilt and Focus.
Epoxy polyester powder coated matt black finish (RAL – 9005) (Customizable as per requirements)
IP Rating : IP20
DMX CHART
1 Channel Mode : Dimmer, 0-100%
WEIGHT & DIMENTIONS
 | Normal Yoke | POS Yoke | Unit
Weight | 7.6 | 9.8 | Kg
Length | 370 |  | mm
Width | 250 |  | mm
Height | 295 |  | mm
ACCESSORIES | 
 | 8 leaf Barndoor
 | 4 leaf Barndoor
 | Softbox
 | Honey comb screens
 | Filter frame
 | Clamps & Spuds
 | Cables
2 of 3
90W – 3200K

## Slide 18
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 5600K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC PERFORMANCE
3 of 3
90W – 3200K

## Slide 19
Canara LED Panel series LED lighting system has been specifically developed for film and video applications that demand extremely color-accurate, high quality light. Utilizing proprietary, state-of-the-art, daylight balanced LEDs, Canara LED Panel creates a high volume of broad spectrum white light, combined with an electronic flicker-free dimmable power supply unit to create a powerful yet economical LED soft light. Perfect for TV studio, Production Studios, Film Recordings & Documentaries etc.,
SOFT PANEL LIGHT
SPECIAL FEATURES
Delivers the High-volume light output.
Double accessories slot for inserting color Filters, Barndoor and other accessories with lock retaining clip.
Fully RDM Compliant when in DMX mode
Electronic universal power supply 100-260 V AC, 50/60 Hz.
Non-glare, diffuser provides uniform, single source light.
Efficient power and thermal management delivers low power consumption and enhanced reliability.
Fanless design perfect for studio application
All metal construction.
No light spill to distract audiences or performers.
Available with pole operated yoke.
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TECHNICAL SPECIFICATIONS
LIGHT SOURCE
Lamp : SMD LED ARRAY
Color temperature (CCT) : 5600K
CRI : > 95, TLCI: > 95, R9 Value: > 95
Color Quality Scale (CQS) : > 95
Lamp life : L70 >50000 Hours @ 55°C
OPTICAL SYSTEM
Beam Angle : 100°
Acrylic milky diffuser 2 mm /3mm thick provides eye pleasant light output.
1 of 3
90W – CCT TUNABLE
MODEL : CAN LED T

## Slide 20
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
ELECTRICAL
Flicker free auto-ranging electronic switch mode power supply 100~240 VAC Nominal, 50/60 Hz
0 to 100% 8 Bit Linear Dimming
Power Factor ≥0.95 @ 230V 50Hz
Main fuse - T12A-250V
Max mains current 3.7A@drawn 1A @ 230V 50Hz
Max LED current drawn 54V DC
Power supply cable: 2 meter 3 Core 1Sq mm FRLS grade PVC cable with IEC Plug
CONTROL
On board Control with 5 No's High Precision Membrane switch with 7 segment display for easy to read status.
USITT DMX512A (RDM Compatible) Control Protocol.
5 pin locking XLR Chasis mount DMX in & through connections
8 bit DMX control, extra soft dimming, for theatrical & Studio use.
PHYSICAL
Aluminum laser cut body
Passive Cooling system with large heatsink, no noise, perfect for TV studios & theatres
Aluminium yoke
Available in Manual and Pole operated system for Pan, Tilt and Focus.
Epoxy polyester powder coated matt black finish (RAL – 9005) (Customizable as per requirements)
IP Rating : IP20
DMX CHART
1 Channel Mode : Dimmer, 0-100%
WEIGHT & DIMENTIONS
 | Normal Yoke | POS Yoke | Unit
Weight | 7.6 | 9.8 | Kg
Length | 370 |  | mm
Width | 250 |  | mm
Height | 295 |  | mm
ACCESSORIES | 
 | 8 leaf Barndoor
 | 4 leaf Barndoor
 | Softbox
 | Honey comb screens
 | Filter frame
 | Clamps & Spuds
 | Cables
2 of 3
90W – CCT TUNABLE

## Slide 21
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
POLAR DIAGRAM - FLOOD
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 3200K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
Photometric Data - Flood @ 50 Degrees - 5600K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC PERFORMANCE
3 of 3
90W – CCT TUNABLE

## Slide 22
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 4700K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC
PERFORMANCE
3 of 3
90W – CCT TUNABLE
SPECTRUM
TM-30

## Slide 23
Canara LED Panel series LED lighting system has been specifically developed for film and video applications that demand extremely color-accurate, high quality light. Utilizing proprietary, state-of-the-art, daylight balanced LEDs, Canara LED Panel creates a high volume of broad spectrum white light, combined with an electronic flicker-free dimmable power supply unit to create a powerful yet economical LED soft light. Perfect for TV studio, Production Studios, Film Recordings & Documentaries etc.,
SOFT PANEL LIGHT
SPECIAL FEATURES
Delivers the High-volume light output.
Double accessories slot for inserting color Filters, Barndoor and other accessories with lock retaining clip.
Fully RDM Compliant when in DMX mode
Electronic universal power supply 100-260 V AC, 50/60 Hz.
Non-glare, diffuser provides uniform, single source light.
Efficient power and thermal management delivers low power consumption and enhanced reliability.
Fanless design perfect for studio application
All metal construction.
No light spill to distract audiences or performers.
Available with pole operated yoke.
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TECHNICAL SPECIFICATIONS
LIGHT SOURCE
Lamp : SMD LED ARRAY
Color temperature (CCT) : 5600K
CRI : > 95, TLCI: > 95, R9 Value: > 95
Color Quality Scale (CQS) : > 95
Lamp life : L70 >50000 Hours @ 55°C
OPTICAL SYSTEM
Beam Angle : 100°
Acrylic milky diffuser 2 mm /3mm thick provides eye pleasant light output.
1 of 3
90W – 5600K
MODEL : CAN LED T

## Slide 24
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
ELECTRICAL
Flicker free auto-ranging electronic switch mode power supply 100~240 VAC Nominal, 50/60 Hz
0 to 100% 8 Bit Linear Dimming
Power Factor ≥0.95 @ 230V 50Hz
Main fuse - T12A-250V
Max mains current 3.7A@drawn 1A @ 230V 50Hz
Max LED current drawn 54V DC
Power supply cable: 2 meter 3 Core 1Sq mm FRLS grade PVC cable with IEC Plug
CONTROL
On board Control with 5 No's High Precision Membrane switch with 7 segment display for easy to read status.
USITT DMX512A (RDM Compatible) Control Protocol.
5 pin locking XLR Chasis mount DMX in & through connections
8 bit DMX control, extra soft dimming, for theatrical & Studio use.
PHYSICAL
Aluminum laser cut body
Passive Cooling system with large heatsink, no noise, perfect for TV studios & theatres
Aluminium yoke
Available in Manual and Pole operated system for Pan, Tilt and Focus.
Epoxy polyester powder coated matt black finish (RAL – 9005) (Customizable as per requirements)
IP Rating : IP20
DMX CHART
1 Channel Mode : Dimmer, 0-100%
WEIGHT & DIMENTIONS
 | Normal Yoke | POS Yoke | Unit
Weight | 7.6 | 9.8 | Kg
Length | 370 |  | mm
Width | 250 |  | mm
Height | 295 |  | mm
ACCESSORIES | 
 | 8 leaf Barndoor
 | 4 leaf Barndoor
 | Softbox
 | Honey comb screens
 | Filter frame
 | Clamps & Spuds
 | Cables
2 of 3
90W – 5600K

## Slide 25
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 5600K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC PERFORMANCE
3 of 3
90W – 5600K

## Slide 26
Canara LED Panel series LED lighting system has been specifically developed for film and video applications that demand extremely color-accurate, high quality light. Utilizing proprietary, state-of-the-art, daylight balanced LEDs, Canara LED Panel creates a high volume of broad spectrum white light, combined with an electronic flicker-free dimmable power supply unit to create a powerful yet economical LED soft light. Perfect for TV studio, Production Studios, Film Recordings & Documentaries etc.,
SOFT PANEL LIGHT
SPECIAL FEATURES
Delivers the High-volume light output.
Double accessories slot for inserting color Filters, Barndoor and other accessories with lock retaining clip.
Fully RDM Compliant when in DMX mode
Electronic universal power supply 100-260 V AC, 50/60 Hz.
Non-glare, diffuser provides uniform, single source light.
Efficient power and thermal management delivers low power consumption and enhanced reliability.
Fanless design perfect for studio application
All metal construction.
No light spill to distract audiences or performers.
Available with pole operated yoke.
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TECHNICAL SPECIFICATIONS
LIGHT SOURCE
Lamp : SMD LED ARRAY
Color temperature (CCT) : 5600K
CRI : > 95, TLCI: > 95, R9 Value: > 95
Color Quality Scale (CQS) : > 95
Lamp life : L70 >50000 Hours @ 55°C
OPTICAL SYSTEM
Beam Angle : 100°
Acrylic milky diffuser 2 mm /3mm thick provides eye pleasant light output.
1 of 3
90W – 3200K
MODEL : CAN LED T

## Slide 27
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
ELECTRICAL
Flicker free auto-ranging electronic switch mode power supply 100~240 VAC Nominal, 50/60 Hz
0 to 100% 8 Bit Linear Dimming
Power Factor ≥0.95 @ 230V 50Hz
Main fuse - T12A-250V
Max mains current 3.7A@drawn 1A @ 230V 50Hz
Max LED current drawn 54V DC
Power supply cable: 2 meter 3 Core 1Sq mm FRLS grade PVC cable with IEC Plug
CONTROL
On board Control with 5 No's High Precision Membrane switch with 7 segment display for easy to read status.
USITT DMX512A (RDM Compatible) Control Protocol.
5 pin locking XLR Chasis mount DMX in & through connections
8 bit DMX control, extra soft dimming, for theatrical & Studio use.
PHYSICAL
Aluminum laser cut body
Passive Cooling system with large heatsink, no noise, perfect for TV studios & theatres
Aluminium yoke
Available in Manual and Pole operated system for Pan, Tilt and Focus.
Epoxy polyester powder coated matt black finish (RAL – 9005) (Customizable as per requirements)
IP Rating : IP20
DMX CHART
1 Channel Mode : Dimmer, 0-100%
WEIGHT & DIMENTIONS
 | Normal Yoke | POS Yoke | Unit
Weight | 7.6 | 9.8 | Kg
Length | 370 |  | mm
Width | 250 |  | mm
Height | 295 |  | mm
ACCESSORIES | 
 | 8 leaf Barndoor
 | 4 leaf Barndoor
 | Softbox
 | Honey comb screens
 | Filter frame
 | Clamps & Spuds
 | Cables
2 of 3
90W – 3200K

## Slide 28
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 5600K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC PERFORMANCE
3 of 3
90W – 3200K

## Slide 29
Canara LED Panel series LED lighting system has been specifically developed for film and video applications that demand extremely color-accurate, high quality light. Utilizing proprietary, state-of-the-art, daylight balanced LEDs, Canara LED Panel creates a high volume of broad spectrum white light, combined with an electronic flicker-free dimmable power supply unit to create a powerful yet economical LED soft light. Perfect for TV studio, Production Studios, Film Recordings & Documentaries etc.,
SOFT PANEL LIGHT
SPECIAL FEATURES
Delivers the High-volume light output.
Double accessories slot for inserting color Filters, Barndoor and other accessories with lock retaining clip.
Fully RDM Compliant when in DMX mode
Electronic universal power supply 100-260 V AC, 50/60 Hz.
Non-glare, diffuser provides uniform, single source light.
Efficient power and thermal management delivers low power consumption and enhanced reliability.
Fanless design perfect for studio application
All metal construction.
No light spill to distract audiences or performers.
Available with pole operated yoke.
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TECHNICAL SPECIFICATIONS
LIGHT SOURCE
Lamp : SMD LED ARRAY
Color temperature (CCT) : 5600K
CRI : > 95, TLCI: > 95, R9 Value: > 95
Color Quality Scale (CQS) : > 95
Lamp life : L70 >50000 Hours @ 55°C
OPTICAL SYSTEM
Beam Angle : 100°
Acrylic milky diffuser 2 mm /3mm thick provides eye pleasant light output.
1 of 3
90W – CCT TUNABLE
MODEL : CAN LED T

## Slide 30
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
ELECTRICAL
Flicker free auto-ranging electronic switch mode power supply 100~240 VAC Nominal, 50/60 Hz
0 to 100% 8 Bit Linear Dimming
Power Factor ≥0.95 @ 230V 50Hz
Main fuse - T12A-250V
Max mains current 3.7A@drawn 1A @ 230V 50Hz
Max LED current drawn 54V DC
Power supply cable: 2 meter 3 Core 1Sq mm FRLS grade PVC cable with IEC Plug
CONTROL
On board Control with 5 No's High Precision Membrane switch with 7 segment display for easy to read status.
USITT DMX512A (RDM Compatible) Control Protocol.
5 pin locking XLR Chasis mount DMX in & through connections
8 bit DMX control, extra soft dimming, for theatrical & Studio use.
PHYSICAL
Aluminum laser cut body
Passive Cooling system with large heatsink, no noise, perfect for TV studios & theatres
Aluminium yoke
Available in Manual and Pole operated system for Pan, Tilt and Focus.
Epoxy polyester powder coated matt black finish (RAL – 9005) (Customizable as per requirements)
IP Rating : IP20
DMX CHART
1 Channel Mode : Dimmer, 0-100%
WEIGHT & DIMENTIONS
 | Normal Yoke | POS Yoke | Unit
Weight | 7.6 | 9.8 | Kg
Length | 370 |  | mm
Width | 250 |  | mm
Height | 295 |  | mm
ACCESSORIES | 
 | 8 leaf Barndoor
 | 4 leaf Barndoor
 | Softbox
 | Honey comb screens
 | Filter frame
 | Clamps & Spuds
 | Cables
2 of 3
90W – CCT TUNABLE

## Slide 31
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
POLAR DIAGRAM - FLOOD
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 3200K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
Photometric Data - Flood @ 50 Degrees - 5600K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC PERFORMANCE
3 of 3
90W – CCT TUNABLE

## Slide 32
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 4700K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC
PERFORMANCE
3 of 3
90W – CCT TUNABLE
SPECTRUM
TM-30

## Slide 33
Canara LED Panel series LED lighting system has been specifically developed for film and video applications that demand extremely color-accurate, high quality light. Utilizing proprietary, state-of-the-art, daylight balanced LEDs, Canara LED Panel creates a high volume of broad spectrum white light, combined with an electronic flicker-free dimmable power supply unit to create a powerful yet economical LED soft light. Perfect for TV studio, Production Studios, Film Recordings & Documentaries etc.,
SOFT PANEL LIGHT
SPECIAL FEATURES
Delivers the High-volume light output.
Double accessories slot for inserting color Filters, Barndoor and other accessories with lock retaining clip.
Fully RDM Compliant when in DMX mode
Electronic universal power supply 100-260 V AC, 50/60 Hz.
Non-glare, diffuser provides uniform, single source light.
Efficient power and thermal management delivers low power consumption and enhanced reliability.
Fanless design perfect for studio application
All metal construction.
No light spill to distract audiences or performers.
Available with pole operated yoke.
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TECHNICAL SPECIFICATIONS
LIGHT SOURCE
Lamp : SMD LED ARRAY
Color temperature (CCT) : 5600K
CRI : > 95, TLCI: > 95, R9 Value: > 95
Color Quality Scale (CQS) : > 95
Lamp life : L70 >50000 Hours @ 55°C
OPTICAL SYSTEM
Beam Angle : 100°
Acrylic milky diffuser 2 mm /3mm thick provides eye pleasant light output.
1 of 3
90W – 5600K
MODEL : CAN LED T

## Slide 34
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
ELECTRICAL
Flicker free auto-ranging electronic switch mode power supply 100~240 VAC Nominal, 50/60 Hz
0 to 100% 8 Bit Linear Dimming
Power Factor ≥0.95 @ 230V 50Hz
Main fuse - T12A-250V
Max mains current 3.7A@drawn 1A @ 230V 50Hz
Max LED current drawn 54V DC
Power supply cable: 2 meter 3 Core 1Sq mm FRLS grade PVC cable with IEC Plug
CONTROL
On board Control with 5 No's High Precision Membrane switch with 7 segment display for easy to read status.
USITT DMX512A (RDM Compatible) Control Protocol.
5 pin locking XLR Chasis mount DMX in & through connections
8 bit DMX control, extra soft dimming, for theatrical & Studio use.
PHYSICAL
Aluminum laser cut body
Passive Cooling system with large heatsink, no noise, perfect for TV studios & theatres
Aluminium yoke
Available in Manual and Pole operated system for Pan, Tilt and Focus.
Epoxy polyester powder coated matt black finish (RAL – 9005) (Customizable as per requirements)
IP Rating : IP20
DMX CHART
1 Channel Mode : Dimmer, 0-100%
WEIGHT & DIMENTIONS
 | Normal Yoke | POS Yoke | Unit
Weight | 7.6 | 9.8 | Kg
Length | 370 |  | mm
Width | 250 |  | mm
Height | 295 |  | mm
ACCESSORIES | 
 | 8 leaf Barndoor
 | 4 leaf Barndoor
 | Softbox
 | Honey comb screens
 | Filter frame
 | Clamps & Spuds
 | Cables
2 of 3
90W – 5600K

## Slide 35
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 5600K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC PERFORMANCE
3 of 3
90W – 5600K

## Slide 36
Canara LED Panel series LED lighting system has been specifically developed for film and video applications that demand extremely color-accurate, high quality light. Utilizing proprietary, state-of-the-art, daylight balanced LEDs, Canara LED Panel creates a high volume of broad spectrum white light, combined with an electronic flicker-free dimmable power supply unit to create a powerful yet economical LED soft light. Perfect for TV studio, Production Studios, Film Recordings & Documentaries etc.,
SOFT PANEL LIGHT
SPECIAL FEATURES
Delivers the High-volume light output.
Double accessories slot for inserting color Filters, Barndoor and other accessories with lock retaining clip.
Fully RDM Compliant when in DMX mode
Electronic universal power supply 100-260 V AC, 50/60 Hz.
Non-glare, diffuser provides uniform, single source light.
Efficient power and thermal management delivers low power consumption and enhanced reliability.
Fanless design perfect for studio application
All metal construction.
No light spill to distract audiences or performers.
Available with pole operated yoke.
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TECHNICAL SPECIFICATIONS
LIGHT SOURCE
Lamp : SMD LED ARRAY
Color temperature (CCT) : 5600K
CRI : > 95, TLCI: > 95, R9 Value: > 95
Color Quality Scale (CQS) : > 95
Lamp life : L70 >50000 Hours @ 55°C
OPTICAL SYSTEM
Beam Angle : 100°
Acrylic milky diffuser 2 mm /3mm thick provides eye pleasant light output.
1 of 3
90W – 3200K
MODEL : CAN LED T

## Slide 37
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
ELECTRICAL
Flicker free auto-ranging electronic switch mode power supply 100~240 VAC Nominal, 50/60 Hz
0 to 100% 8 Bit Linear Dimming
Power Factor ≥0.95 @ 230V 50Hz
Main fuse - T12A-250V
Max mains current 3.7A@drawn 1A @ 230V 50Hz
Max LED current drawn 54V DC
Power supply cable: 2 meter 3 Core 1Sq mm FRLS grade PVC cable with IEC Plug
CONTROL
On board Control with 5 No's High Precision Membrane switch with 7 segment display for easy to read status.
USITT DMX512A (RDM Compatible) Control Protocol.
5 pin locking XLR Chasis mount DMX in & through connections
8 bit DMX control, extra soft dimming, for theatrical & Studio use.
PHYSICAL
Aluminum laser cut body
Passive Cooling system with large heatsink, no noise, perfect for TV studios & theatres
Aluminium yoke
Available in Manual and Pole operated system for Pan, Tilt and Focus.
Epoxy polyester powder coated matt black finish (RAL – 9005) (Customizable as per requirements)
IP Rating : IP20
DMX CHART
1 Channel Mode : Dimmer, 0-100%
WEIGHT & DIMENTIONS
 | Normal Yoke | POS Yoke | Unit
Weight | 7.6 | 9.8 | Kg
Length | 370 |  | mm
Width | 250 |  | mm
Height | 295 |  | mm
ACCESSORIES | 
 | 8 leaf Barndoor
 | 4 leaf Barndoor
 | Softbox
 | Honey comb screens
 | Filter frame
 | Clamps & Spuds
 | Cables
2 of 3
90W – 3200K

## Slide 38
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 5600K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC PERFORMANCE
3 of 3
90W – 3200K

## Slide 39
Canara LED Panel series LED lighting system has been specifically developed for film and video applications that demand extremely color-accurate, high quality light. Utilizing proprietary, state-of-the-art, daylight balanced LEDs, Canara LED Panel creates a high volume of broad spectrum white light, combined with an electronic flicker-free dimmable power supply unit to create a powerful yet economical LED soft light. Perfect for TV studio, Production Studios, Film Recordings & Documentaries etc.,
SOFT PANEL LIGHT
SPECIAL FEATURES
Delivers the High-volume light output.
Double accessories slot for inserting color Filters, Barndoor and other accessories with lock retaining clip.
Fully RDM Compliant when in DMX mode
Electronic universal power supply 100-260 V AC, 50/60 Hz.
Non-glare, diffuser provides uniform, single source light.
Efficient power and thermal management delivers low power consumption and enhanced reliability.
Fanless design perfect for studio application
All metal construction.
No light spill to distract audiences or performers.
Available with pole operated yoke.
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TECHNICAL SPECIFICATIONS
LIGHT SOURCE
Lamp : SMD LED ARRAY
Color temperature (CCT) : 5600K
CRI : > 95, TLCI: > 95, R9 Value: > 95
Color Quality Scale (CQS) : > 95
Lamp life : L70 >50000 Hours @ 55°C
OPTICAL SYSTEM
Beam Angle : 100°
Acrylic milky diffuser 2 mm /3mm thick provides eye pleasant light output.
1 of 3
90W – CCT TUNABLE
MODEL : CAN LED T

## Slide 40
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
ELECTRICAL
Flicker free auto-ranging electronic switch mode power supply 100~240 VAC Nominal, 50/60 Hz
0 to 100% 8 Bit Linear Dimming
Power Factor ≥0.95 @ 230V 50Hz
Main fuse - T12A-250V
Max mains current 3.7A@drawn 1A @ 230V 50Hz
Max LED current drawn 54V DC
Power supply cable: 2 meter 3 Core 1Sq mm FRLS grade PVC cable with IEC Plug
CONTROL
On board Control with 5 No's High Precision Membrane switch with 7 segment display for easy to read status.
USITT DMX512A (RDM Compatible) Control Protocol.
5 pin locking XLR Chasis mount DMX in & through connections
8 bit DMX control, extra soft dimming, for theatrical & Studio use.
PHYSICAL
Aluminum laser cut body
Passive Cooling system with large heatsink, no noise, perfect for TV studios & theatres
Aluminium yoke
Available in Manual and Pole operated system for Pan, Tilt and Focus.
Epoxy polyester powder coated matt black finish (RAL – 9005) (Customizable as per requirements)
IP Rating : IP20
DMX CHART
1 Channel Mode : Dimmer, 0-100%
WEIGHT & DIMENTIONS
 | Normal Yoke | POS Yoke | Unit
Weight | 7.6 | 9.8 | Kg
Length | 370 |  | mm
Width | 250 |  | mm
Height | 295 |  | mm
ACCESSORIES | 
 | 8 leaf Barndoor
 | 4 leaf Barndoor
 | Softbox
 | Honey comb screens
 | Filter frame
 | Clamps & Spuds
 | Cables
2 of 3
90W – CCT TUNABLE

## Slide 41
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
POLAR DIAGRAM - FLOOD
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 3200K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
Photometric Data - Flood @ 50 Degrees - 5600K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC PERFORMANCE
3 of 3
90W – CCT TUNABLE

## Slide 42
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 4700K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC
PERFORMANCE
3 of 3
90W – CCT TUNABLE
SPECTRUM
TM-30

## Slide 43
Canara LED Panel series LED lighting system has been specifically developed for film and video applications that demand extremely color-accurate, high quality light. Utilizing proprietary, state-of-the-art, daylight balanced LEDs, Canara LED Panel creates a high volume of broad spectrum white light, combined with an electronic flicker-free dimmable power supply unit to create a powerful yet economical LED soft light. Perfect for TV studio, Production Studios, Film Recordings & Documentaries etc.,
SOFT PANEL LIGHT
SPECIAL FEATURES
Delivers the High-volume light output.
Double accessories slot for inserting color Filters, Barndoor and other accessories with lock retaining clip.
Fully RDM Compliant when in DMX mode
Electronic universal power supply 100-260 V AC, 50/60 Hz.
Non-glare, diffuser provides uniform, single source light.
Efficient power and thermal management delivers low power consumption and enhanced reliability.
Fanless design perfect for studio application
All metal construction.
No light spill to distract audiences or performers.
Available with pole operated yoke.
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TECHNICAL SPECIFICATIONS
LIGHT SOURCE
Lamp : SMD LED ARRAY
Color temperature (CCT) : 5600K
CRI : > 95, TLCI: > 95, R9 Value: > 95
Color Quality Scale (CQS) : > 95
Lamp life : L70 >50000 Hours @ 55°C
OPTICAL SYSTEM
Beam Angle : 100°
Acrylic milky diffuser 2 mm /3mm thick provides eye pleasant light output.
1 of 3
90W – 5600K
MODEL : CAN LED T

## Slide 44
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
ELECTRICAL
Flicker free auto-ranging electronic switch mode power supply 100~240 VAC Nominal, 50/60 Hz
0 to 100% 8 Bit Linear Dimming
Power Factor ≥0.95 @ 230V 50Hz
Main fuse - T12A-250V
Max mains current 3.7A@drawn 1A @ 230V 50Hz
Max LED current drawn 54V DC
Power supply cable: 2 meter 3 Core 1Sq mm FRLS grade PVC cable with IEC Plug
CONTROL
On board Control with 5 No's High Precision Membrane switch with 7 segment display for easy to read status.
USITT DMX512A (RDM Compatible) Control Protocol.
5 pin locking XLR Chasis mount DMX in & through connections
8 bit DMX control, extra soft dimming, for theatrical & Studio use.
PHYSICAL
Aluminum laser cut body
Passive Cooling system with large heatsink, no noise, perfect for TV studios & theatres
Aluminium yoke
Available in Manual and Pole operated system for Pan, Tilt and Focus.
Epoxy polyester powder coated matt black finish (RAL – 9005) (Customizable as per requirements)
IP Rating : IP20
DMX CHART
1 Channel Mode : Dimmer, 0-100%
WEIGHT & DIMENTIONS
 | Normal Yoke | POS Yoke | Unit
Weight | 7.6 | 9.8 | Kg
Length | 370 |  | mm
Width | 250 |  | mm
Height | 295 |  | mm
ACCESSORIES | 
 | 8 leaf Barndoor
 | 4 leaf Barndoor
 | Softbox
 | Honey comb screens
 | Filter frame
 | Clamps & Spuds
 | Cables
2 of 3
90W – 5600K

## Slide 45
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 5600K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC PERFORMANCE
3 of 3
90W – 5600K

## Slide 46
Canara LED Panel series LED lighting system has been specifically developed for film and video applications that demand extremely color-accurate, high quality light. Utilizing proprietary, state-of-the-art, daylight balanced LEDs, Canara LED Panel creates a high volume of broad spectrum white light, combined with an electronic flicker-free dimmable power supply unit to create a powerful yet economical LED soft light. Perfect for TV studio, Production Studios, Film Recordings & Documentaries etc.,
SOFT PANEL LIGHT
SPECIAL FEATURES
Delivers the High-volume light output.
Double accessories slot for inserting color Filters, Barndoor and other accessories with lock retaining clip.
Fully RDM Compliant when in DMX mode
Electronic universal power supply 100-260 V AC, 50/60 Hz.
Non-glare, diffuser provides uniform, single source light.
Efficient power and thermal management delivers low power consumption and enhanced reliability.
Fanless design perfect for studio application
All metal construction.
No light spill to distract audiences or performers.
Available with pole operated yoke.
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TECHNICAL SPECIFICATIONS
LIGHT SOURCE
Lamp : SMD LED ARRAY
Color temperature (CCT) : 5600K
CRI : > 95, TLCI: > 95, R9 Value: > 95
Color Quality Scale (CQS) : > 95
Lamp life : L70 >50000 Hours @ 55°C
OPTICAL SYSTEM
Beam Angle : 100°
Acrylic milky diffuser 2 mm /3mm thick provides eye pleasant light output.
1 of 3
90W – 3200K
MODEL : CAN LED T

## Slide 47
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
ELECTRICAL
Flicker free auto-ranging electronic switch mode power supply 100~240 VAC Nominal, 50/60 Hz
0 to 100% 8 Bit Linear Dimming
Power Factor ≥0.95 @ 230V 50Hz
Main fuse - T12A-250V
Max mains current 3.7A@drawn 1A @ 230V 50Hz
Max LED current drawn 54V DC
Power supply cable: 2 meter 3 Core 1Sq mm FRLS grade PVC cable with IEC Plug
CONTROL
On board Control with 5 No's High Precision Membrane switch with 7 segment display for easy to read status.
USITT DMX512A (RDM Compatible) Control Protocol.
5 pin locking XLR Chasis mount DMX in & through connections
8 bit DMX control, extra soft dimming, for theatrical & Studio use.
PHYSICAL
Aluminum laser cut body
Passive Cooling system with large heatsink, no noise, perfect for TV studios & theatres
Aluminium yoke
Available in Manual and Pole operated system for Pan, Tilt and Focus.
Epoxy polyester powder coated matt black finish (RAL – 9005) (Customizable as per requirements)
IP Rating : IP20
DMX CHART
1 Channel Mode : Dimmer, 0-100%
WEIGHT & DIMENTIONS
 | Normal Yoke | POS Yoke | Unit
Weight | 7.6 | 9.8 | Kg
Length | 370 |  | mm
Width | 250 |  | mm
Height | 295 |  | mm
ACCESSORIES | 
 | 8 leaf Barndoor
 | 4 leaf Barndoor
 | Softbox
 | Honey comb screens
 | Filter frame
 | Clamps & Spuds
 | Cables
2 of 3
90W – 3200K

## Slide 48
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 5600K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC PERFORMANCE
3 of 3
90W – 3200K

## Slide 49
Canara LED Panel series LED lighting system has been specifically developed for film and video applications that demand extremely color-accurate, high quality light. Utilizing proprietary, state-of-the-art, daylight balanced LEDs, Canara LED Panel creates a high volume of broad spectrum white light, combined with an electronic flicker-free dimmable power supply unit to create a powerful yet economical LED soft light. Perfect for TV studio, Production Studios, Film Recordings & Documentaries etc.,
SOFT PANEL LIGHT
SPECIAL FEATURES
Delivers the High-volume light output.
Double accessories slot for inserting color Filters, Barndoor and other accessories with lock retaining clip.
Fully RDM Compliant when in DMX mode
Electronic universal power supply 100-260 V AC, 50/60 Hz.
Non-glare, diffuser provides uniform, single source light.
Efficient power and thermal management delivers low power consumption and enhanced reliability.
Fanless design perfect for studio application
All metal construction.
No light spill to distract audiences or performers.
Available with pole operated yoke.
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
TECHNICAL SPECIFICATIONS
LIGHT SOURCE
Lamp : SMD LED ARRAY
Color temperature (CCT) : 5600K
CRI : > 95, TLCI: > 95, R9 Value: > 95
Color Quality Scale (CQS) : > 95
Lamp life : L70 >50000 Hours @ 55°C
OPTICAL SYSTEM
Beam Angle : 100°
Acrylic milky diffuser 2 mm /3mm thick provides eye pleasant light output.
1 of 3
90W – CCT TUNABLE
MODEL : CAN LED T

## Slide 50
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
ELECTRICAL
Flicker free auto-ranging electronic switch mode power supply 100~240 VAC Nominal, 50/60 Hz
0 to 100% 8 Bit Linear Dimming
Power Factor ≥0.95 @ 230V 50Hz
Main fuse - T12A-250V
Max mains current 3.7A@drawn 1A @ 230V 50Hz
Max LED current drawn 54V DC
Power supply cable: 2 meter 3 Core 1Sq mm FRLS grade PVC cable with IEC Plug
CONTROL
On board Control with 5 No's High Precision Membrane switch with 7 segment display for easy to read status.
USITT DMX512A (RDM Compatible) Control Protocol.
5 pin locking XLR Chasis mount DMX in & through connections
8 bit DMX control, extra soft dimming, for theatrical & Studio use.
PHYSICAL
Aluminum laser cut body
Passive Cooling system with large heatsink, no noise, perfect for TV studios & theatres
Aluminium yoke
Available in Manual and Pole operated system for Pan, Tilt and Focus.
Epoxy polyester powder coated matt black finish (RAL – 9005) (Customizable as per requirements)
IP Rating : IP20
DMX CHART
1 Channel Mode : Dimmer, 0-100%
WEIGHT & DIMENTIONS
 | Normal Yoke | POS Yoke | Unit
Weight | 7.6 | 9.8 | Kg
Length | 370 |  | mm
Width | 250 |  | mm
Height | 295 |  | mm
ACCESSORIES | 
 | 8 leaf Barndoor
 | 4 leaf Barndoor
 | Softbox
 | Honey comb screens
 | Filter frame
 | Clamps & Spuds
 | Cables
2 of 3
90W – CCT TUNABLE

## Slide 51
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
POLAR DIAGRAM - FLOOD
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 3200K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
Photometric Data - Flood @ 50 Degrees - 5600K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC PERFORMANCE
3 of 3
90W – CCT TUNABLE

## Slide 52
SOFT PANEL LIGHT
We innovate continuously to improve specifications, design, manufacturing techniques etc. hence technical data and offerings are subject to change without prior notice. Individual test results may vary. Results based on a representative sample in Canara inventory.
SPECTRUM
TM-30
Design, Manufacture and Tested at Canara Lighting Industries Pvt. Ltd. Mulky-Kinnigoli Airport Road Mangalore 574 150. India.
Photometric Data - Flood @ 100 Degrees - 4700K |  |  |  |  |  | 
Throw Distance | (m) | 1 | 2 | 3 | 5 | 7
 | (ft) |  |  |  |  | 
Beam Diameter | (m) |  |  |  |  | 
 | (ft) |  |  |  |  | 
Illumination | (lux) | 99999 | 99999 | 99999 | 99999 | 99999
 | (fc) |  |  |  |  | 
POLAR DIAGRAM – FLOOD
PHOTOMETRIC
PERFORMANCE
3 of 3
90W – CCT TUNABLE
SPECTRUM
TM-30

## Slide 53
We innovate continuously, hence data & design given are subject to change without notice.
Individual test results may vary. Results based on a representative sample in Canara inventory.
LED LIGHTS